2019 Greenhouse Experiments Data Preparation and Analyses
(aka, Clay’s trail of breadcrumbs through the forest...)
Clay Bliss

** Note: A summary of important dates and irrigation schedule can be found here: general/2019_greenhouse_experiment_timeline_notes.odt

Part 1: Data Preparation and Organization

1.1 Continuous time-series raw data files converted to 15-minute means data files.

Variables include: RH, air/soil temp, wind speed, PAR (both arduino and line-quantum), pyranometer, atmospheric pressure, scale weights, leaf temperature.

This was done separately for experiments 1 & 2, see these files (adapted from Sean’s “figures_and_stats_v1.R”):

Sean’s data (everything but scale weights and leaf temps):

first_summer_experiment/scripts/clay_R_scripts/data_prep/exp1_aggregate_raw_data_15min.R

second_fall_experiment/scripts/clay_R_scripts/data_prep/exp2_aggregate_raw_data_15min.R

Clay’s data (scale weights and leaf temps):

first_summer_experiment/scripts/clay_R_scripts/data_prep/scale_data_prep.R

first_summer_experiment/scripts/clay_R_scripts/data_prep/leaf_thermistor_data_prep.R

second_fall_experiment/scripts/clay_R_scripts/data_prep/scale_data_prep.R

second_fall_experiment/scripts/clay_R_scripts/data_prep/leaf_thermistor_data_prep.R

General Notes:

- Some basic QA/QC checks are done in these scripts; mostly visually inspecting the timeseries of each variable. Obviously bad data are changed to ‘NA’ (see below). These checks are done on the raw data (before15-minute aggregation), except for the wind data (since the wind data is not temperature-compensated until after it is aggregated). See ‘QAQC Notes’ below for details.
- Extensive QAQC and data quality flags are added in the leaf thermistor and scale data scripts.
- For experiment 2, the treatment start/end times are defined at the top of script
- For experiment 2, the LED PAR contribution (225 umol/m2/s) is added to the PAR variables in this script
- TODO: For experiment 1, Sean needs to confirm that the wind sensor columns are properly assigned (both sensor height and treatments). Sean also should confirm whether his dataloggers were set to MDT or MST (I assumed MST and set the times back 1 hour in the above script, to make them match experiment 2 which was in MST). Also, the soil sensors need to be assigned to blocks/treatments.
- For experiment 1, no data for: sht_1_low_temp/rh, line_quantum_PAR

QA/QC Notes
For both experiments, par1_n, par2_s, pyr1_n, pyr2_s all have many values below zero (mostly or all during non-daylight hours). So far for the modeling/analyses I’ve done, I’ve just been converting anything below zero to zero. It might be worth looking into a more sophisticated approach to see if (a) the daylight readings are also shifted down, relative to what they are expected to be (or relative to comparable PAR/pyranometer data); and if so, (b) we can figure out a method to adjust the data. Perhaps this would be as simple as shifting up by a constant; would need to ask Sean if he thinks about this, since I don’t know how those sensors work.
- Experiment 1
  - par1/par2 track closely, but par1_n is much noisier data. pyr1/pyr2 track closely. All 4 variables have several values < 0 but only in non-daylight hours (I think); otherwise data look ok.
  - Air temp: am2320 and sht2_low track very closely. The temp sensor in the datalogger box (bmp_box_temp) tracks the other 2 reasonably well, but is consistently hotter. All data look ok.
  - RH (both sensors) looks reasonable and track together, but notably higher values and larger diurnal swings than in experiment 2. I’m guessing this is because we didn’t use box fans in the 1st experiment? Also, the upper sensor (am2320_high) generally reads a bit lower than the lower sensor (sht2_low), which makes sense since the lower one was in the canopy (I believe) and the upper was above the canopy.
  - Soil temp: I omitted some obvious outliers from the raw data, values < 10 or > 60 deg C, before aggregating.
- Experiment 2
  - See this folder for examples of bad or strange data discussed below: /second_fall_experiment/figures/clay_figures/QAQC
  - All of the “rh” dataframe sensors’ data on 8/21 looked bad, so I deleted it.
  - The largest issue found was with the par1_n and par2_s data. The par2_s data had several periods of extremely noisy data, with impossibly large/small values (swings between 10000 and -10000 in a day) that I converted to NA (since even the 15-min means were obviously wrong). The par1_n data looked much better overall, but roughly the first half of the experiment’s data were much noisier than the second half. TODO: I wasn’t sure what to do about this. It may or may not be an issue in analyzing the 15-minute data.
  - The pyranometer data (pyr1_n, pyr2_s) looked good overall, but both sensors have an odd trend of the “baseline” or lower values (and maybe all values, not sure?) declining after about the 2-3rd week of November. TODO: I wasn’t sure what to do about this. It may or may not be an issue in analyzing the 15-minute data.

1.2 Combine all 15-minute means data (plus other derived variables) into one master, plant-level dataframe.

first_summer_experiment/scripts/clay_R_scripts/data_prep/exp1_combine_data_plant_level.R

second_fall_experiment/scripts/clay_R_scripts/data_prep/exp2_combine_data_plant_level.R

Some notes:
Poor quality (flagged) data are changed to NA values in these scripts before merging to other data, for leaf temperature and transpiration data.
- For both experiment 1 and 2, derived variables include:
  - Soil water potential, calculated in this script:
    second_fall_experiment/scripts/clay_R_scripts/analysis/mass_balance/01_scale_mass_balance.R
  - Mean leaf temperature (across all available heights) and highest-available leaf temperature. Leaf thermistors were moved throughout the experiment (at the start of the experiment plants weren’t tall enough and towards the end, the lower leaves died). Having these derived variables are useful in modeling.
  - Transpiration (scaled to leaf area) and leaf area; see below for description/scripts used
  - VPD_air_low, VPD_air_high, VPD_leaf
  - Daily irrigation (“irrig”; L) given on previous evening/night, plus cummulative sums and cummulative mean irrigation (since planting).

Part 2: Data Analysis

2.1 Transpiration

second_fall_experiment/scripts/clay_R_scripts/analysis/model_transpiration/scale_transpiration_calculation.R

- Raw transpiration (mg/s) was calculated for each plant , using 15-min mean scale weights and taking 1st-order differences. Any scale data that was flagged as likely to be poor quality, or was within 3 hours after irrigation, or had a gap other than 15-minutes was given a value of NA for transpiration.
- Transpiration was scaled to plant leaf area, using the mean plant leaf area for each block/treatment (calculated on a daily basis; see below), to obtain units of mg/m2/s.
- Link to Clay’s Lasso modeling:
second_fall_experiment/scripts/clay_R_scripts/analysis/model_transpiration/01_model_transpiration_lasso.R

2.2 Leaf Area (random forests and piecewise-linear regression)

2.2.1 – Leaf Area, 2nd Experiment

second_fall_experiment/scripts/clay_R_scripts/analysis/model_leaf_area/01_model_leaf_area.R

- The basic idea was to use the leaf length and width from the harvested plants to build and validate a model predicting leaf area; and then use this on the non-harvest plant measurement data to predict leaf area.
- First, since the non-harvest measurements do not include leaf length (but include leaf width), I tuned a random forest model (10-fold cross-validation) to predict leaf length from leaf width (plus other variables). This resulted in a model with cross-validation RMSE = 8.05 cm, R2=0.85. The relative importance of predictors was: leaf_order_reverse (1), leaf_width_cm (0.84) and leaf_order (0.32). This performed significantly better than a linear model.
- Next, I used the predicted leaf lengths output from the above model, plus other variables, as input to a random forest to predict leaf area (again using 10-fold cross-validation). The resulting tuned model had cross-validation RMSE=48.1 cm2, R2=0.95. The relative importance of predictors was leaf_length_predicted (1), leaf_width (0.53), leaf_order_reverse (0.09). (A model fit using measured leaf widths, when available, performed no better than this.) After scaling these predicted leaf area to total plant leaf area and comparing to actual (measured) leaf area, and fitting a linear model, the R2=0.99, with slope = 1.01, indicating a near-perfect fit between measured and predicted total plant leaf area.
- The leaf length model random forest and, in turn, the leaf area random forest model, were used on to obtain estimated leaf area (for each leaf) on the non-harvest dataset. (Note: I used measured leaf lengths as input, when available (harvest data), and predicted leaf lengths when not (non-harvest data)).
- Finally, the the harvest and non-harvest data was pooled, and the mean plant leaf area (cm2) was calculated for each block and sampling date. Then, a piecewise-linear model was used (fitting a straight line between each of these points) to interpolate the mean plant leaf area (by block) for every day in the experiment. See result below. (For dates before any leaf measurements were taken, I simply extended flat lines back in time. You can see this in the virgin plants, W block, between 11/27 and 12/6).

2.2.1 – Leaf Area, 1st Experiment

first_summer_experiment/scripts/clay_R_scripts/analysis/model_leaf_area/01_model_leaf_area_both_experiments.R

- Instead of using the random forests and piecewise-linear model constructed (above), I used the leaf area data from the first 59 days of the 2nd experiment to make a linear model that could be applied to the 1st experiment. (There were 2 days with leaf area values within the first 59 days of the 2nd experiment; one set of actual leaf area measurements on day 52 (border plants) and another set of modeled leaf area values on day 59).
- There were two predictors in this linear model. The first was cummulative growing degree days (I used Argus greenhouse air temperature data to calculate GDD, since there were gaps in Sean’s air temperature data and the Argus data was highly correlated with Sean’s air temp data). The second predictor was treatment (the treatment variable had only 2 levels: “dry” for full_drought and “wet” for both well_watered and moderate_drought (this resulted in better separation of leaf areas in the treatments). The resulting linear model had adjusted R2=0.54 and p-values <= 0.02 for both predictors.
- Finally, I used this linear model to predict leaf area in each set of treatments (“wet” and “dry” as defined above), in experiment 1. The output predictions are saved here:
  first_summer_experiment/scripts/clay_R_scripts/analysis/model_leaf_area/plant_leaf_area_predictions.rds

Also, there were measurements on 4 plants of leaf width/length in 1st experiment, so I was able to somewhat validate the predictions of the simpler leaf area model (based on cummulative GDD and treatment) to what the random forest model would predict (based on leaf width/length). These had pretty good agreement, see R script cited above (01_model_leaf_area_both_experiments.R).

2.3 Plant above-ground wet weight modeling / Soil water potential modeling

2.3.1 – Plant weight / Soil water potential, 2nd Experiment

second_fall_experiment/scripts/clay_R_scripts/analysis/mass_balance/01_scale_mass_balance.R

First, I fit a linear model to the final (12/12) harvest data, to predict plant wet weights (n=16) using dry weight and block. The R2=0.94 and RMSE=19.4 g. The model was much better than a linear model using only dry weight as the predictor (R2=0.45).

lm(formula = wet_weight_g ~ dry_weight_g + block, data = bm3)

Residuals:
    Min 1Q Median 3Q Max
-31.591 -18.685 -2.058 14.484 35.708

Coefficients:
        Estimate Std. Error t value Pr(>|t|)
(Intercept) -105.9375 61.1390 -1.733 0.111
dry_weight_g 3.4450 0.3498 9.848 8.61e-07 ***
blockM 107.2533 17.6505 6.076 8.00e-05 ***
blockV 17.9153 16.9867 1.055 0.314
blockW 156.0652 17.1523 9.099 1.88e-06 ***
---
Signif. codes: 0 ‘***’ 0.001 ‘**’ 0.01 ‘*’ 0.05 ‘.’ 0.1 ‘ ’ 1

Residual standard error: 23.99 on 11 degrees of freedom
Multiple R-squared: 0.9548, Adjusted R-squared: 0.9384
F-statistic: 58.13 on 4 and 11 DF, p-value: 2.498e-07
- Next, I used the above model to estimate wet weights for the harvested plants on the 2 previous harvest dates (10/30, 11/15). Then, I combined these estimates with the actual measured wet weights (12/12) and added an observation of weight zero at time zero (the date seed were planted, on 9/9) for each plant. I then fit a logistic curve separately to each block’s wet weight data over the course of the experiment (for the virgin plants, there was only 1 harvest on 12/12 so I simply fit a line between zero starting weight and the mean ending weights).
- I used the open-source app “Enguage Digitizer” to extract the data points from the vanBavel et al. Water release curve, and then fit a curve to the points (in R) using a loess smoother.
- Next I calculated the soil wet weight for each of the 12 plants on scales, at 15 minute intervals, by subtracting from the scale weights the weight of soil sensors and the pot itself, and the plant wet weight (daily mean weights by block, calculated as above).
- I then (for each plant) calculated the saturated (field capacity) soil wet weights, using the most-recent available scale data before drought treatments began, after pots were fully irrigated but drained (on 10/22 at 02:00). These saturated wet weights were used to estimate the dry weight (and volume) of the soil, by assuming a water content of 0.45 at saturation (per vanBavel for containers of similar size), and a bulk density of 0.65 (per Garret’s measurements). The calculation was:
  - Dry soil mass = Saturated soil mass / (1 + 0.45/0.65)
  - Dry soil volume = Dry soil mass / 0.65
- Next I calculated the volumetric water content for each pot every 15 minutes as:
  - WC = (Current soil wet weight, time ‘t’ - Dry soil weight) / dry soil volume
  - Note: the numerator is simply the weight (or volume) of water in the soil at time ‘t’
- Finally, I converted soil water content to water potential using the loess model fit to the vanBavel water-release curve (see above).
- Note: for the virgin plants, I used the same procedure as above, but the saturated soil weights were calculated using the pot wet weights on 11/28 02:00.

2.3.2 – Plant weight / Soil water potential, 1st Experiment

first_summer_experiment/scripts/clay_R_scripts/analysis/mass_balance/01_scale_mass_balance.R

- The calculation of soil water potential was done almost the same way as in the 2nd experiment, except we did not have any measurements of above-ground biomass (wet or dry) from the 1st experiment, so I just assumed the mean above-ground wet weight for each treatment was the same as in the 2nd experiment. I also did not know the mass of the sensors in each pot, so I just subtracted the mean sensor weight measured in 2nd experiment.
- The predictions do not look believable, and I’m not sure why. It could be because the irrigation amounts differed slightly between the 2 experiments. (see here for figures):
  first_summer_experiment/figures/clay_figures/mass_balance/modeled_soil_water_potential

2.4 Leaf Water Potential model

second_fall_experiment/scripts/clay_R_scripts/analysis/model_psi_leaf/01_model_psi_leaf.R

- I used Lasso regression (repeated cross-validation; see script) to select a subset of 7 useful parameters to predict psi_leaf, and then from these, used best subsets to narrow down to 4 parameters. (I also omitted “leaftemp_mean” because although it was a powerful predictor, it was highly collinear with “sht2_low_temp”, and had fewer data points than the latter in both experiment 1 and 2).
- The final linear model was: psi_leaf ~ irrig + minutes + sht2_low_temp + sht2_low_rh. On the full dataset of 227 pressure bomb readings, it had an adjusted R2=0.87 and RMSE=0.16 (MPa). The model itself is saved here (and is used in the data compilation script to add psi_leaf variable):
  second_fall_experiment/scripts/clay_R_scripts/analysis/model_psi_leaf/psi_leaf_linear_model.rds
- Note: Because this model uses “irrig” (irrigation amount in mL) as a predictor (rather than a dummy variable for treatment), the predictions for the virgin_drought and full_drought plants are identical. The reason I used “irrig” rather than “treatment” is so the model would be useful in the 1st exper	iment (since there was no virgin_drought there).
- Below is an example of some predictions from Experiment 2 (lines are predictions; circles are pressure bomb readings). Note that a PAR variable could be added to the model, which might help smooth out some of the precipitous drops in psi_leaf at night. (I didn’t add one since I wasn’t sure which variable would be used in Experiment 1.)

NOTE: The predictions of psi_leaf for the 1st experiment seem ok, but for some reason all 3 treatments have the same predictions...not sure why. Guessing the irrigation effect is too small to carry over to the first experiment?? Sorry, I didn’t have time to figure this out.