Clayton Bliss
Gleason Greenhouse Experiment, Fall-Winter 2019
Important Dates and Notes

Expiriment 1

7-11. Planted seeds. Irrigation ~ 625 mL (9 minutes @ 1 gph)

**NOTE: At some point (not recorded ??) I changed the irrigation to 15 minutes with 4 L/hr emitters, or ca. 1000 mL).

8-14. Scales 1-4 logging.
8-21. Wind sensors logging.
8-22. Scales 5-8 logging.
8-23. Psychrometers placed on a plant in each treatment.
8-24. All 12 plants on scales logging. Treatments began (with irrigation on at 18:00 MST).
9-3. End of experiment.

Expiriment 2

9-9. Plant date, 72 main block plants (not including “virgin” plants). Hand watering plants.

9-13. Irrigation set to water for 5 minutes @ 2 gallons/hour, or 630 mL/day. Set to water at 19:00 MST.

9-18 and 9-19. Planted 8 more “virgin” plants in 2 rows on east side.

9/25. LEDs turned on @ 11:00. Programmed to be on between 04:00 to 20:00 daily. NOTE: The time in the greenhouse control computer system is about 40 minutes ahead of the actual current time, at least as of 11/21. Not sure if this extends back prior to the MDT to MST transition (11/3 at 02:00).

10-17. Changed emitter type to 4 L/hr. Changed irrigation to 14 minutes/day, which equals ca. 1 L/day.

10-21 and 10-22. Covered pots with plastic wrap (didn’t record times). Do we want to use scale data before this? (Maybe just to check and see how different the transpiration estimates are before/after?)

10-24. Treatment 1 began:
W block = fully watered, 10 minutes/day @ 4 L/hr, or ~ 750 mL/day **See below, changed to	15 minutes/day on 10-30.
M block = moderate drought, 5 minutes/day @ 4 L/hr, or ~375 mL/day
D block = full drought, 2 minutes/day @ 4 L/hr, or ~ 150 mL/day

10-28. Changed irrigation start time from 19:00 to 20:05 (since LEDs turn off at 20:00). Clock still set to MDT.

10-28. Box fans turned on at 16:00 MDT.

10-30. Increased fully-watered treatment irrigation to 15 minutes @ 4 L/hr, or ~ 1 L/day.

11-4. Treatment 2 began:
W block = full drought, 2 minutes/day @ 4 L/hr, or ~ 150 mL/day
M block = moderate drought, 5 minutes/day @ 4 L/hr, or ~375 mL/day
D block = fully watered, 15 minutes/day @ 4 L/hr, or ~ 1 L/day

11-4. Noticed that both scale logger Raspberry Pis were 1 hour ahead, presumably because the time zone on the Rpi had been set to MST. I downloaded the data and then reset the clock to the current (MDT) time.

11-21. Greenhouse temperature settings changed (1st period, from 05:00 to 21:00). Cooling threshold remained at 85 F, but heating threshold was changed from 71.6 F to 75 F.

11-27.
Replaced 8 of the W block plants (including all 4 on scales) with the 8 virgin plants.
- Noticed a leaf directly in front of (blocking) the lowest wind sensor in the M block. Moved leaf out of way at 13:51.
- Disconnected Garret’s soil sensors in W block
- Moved Sean’s soil temperature sensor from pot W-11 to W-29 (virgin)
- Set irrigation timer clock back 1 hour (forgot to do this for daylight savings change on 11-3). Watering time is the same, 20:05 (so now 1 hour earlier than before...this was a mistake because I had a brain fart, I was thinking it would be 1 hour later).
- Treatment 3 began:
  - W block = virgin plants, full drought, 2 minutes/day @ 4 L/hr, or ~ 150 mL/day
  - M block = fully watered, 15 minutes/day @ 4 L/hr, or ~ 1 L/day
  - D block = full drought, full drought, 2 minutes/day @ 4 L/hr, or ~ 150 mL/day
  - Note: plants that were in W block are now getting fully watered, 15 minutes/day @ 4 L/hr, or ~ 1 L/day (but these plants are not on scales any more).

12-3. Noticed the upper wind sensor in block M had leaves directly in front (blocking) it. I moved them out of the way at ca 11:50.

12-5.
- Turned box fans off, ca. 9:30, since Clay/Kevin were taking thermal imagery of thermistors and it wind made it difficult. Turned back on ca. 13:00.
- Ceiling (‘HAF’) fans turned off, ca. 10:30. Turned back on ca. 13:00.
- LEDs turned off, ca. 10:30-10:45 (Sean/Jared taking Licor measurements)

12-10. LEDs turned off at 16:50, Clay took pressure bomb measurements in the dark at 18:00 today and 06:20 tomorrow.

12-11. LEDs turned back on at 07:14.

12-12. End of experiment, all plants harvested.